## Slide 1: The importance of geoelectric fields
Specifying the natural environment risk for GIC
Notes: I’ve used the RAL Space template because I just adapted from my September 2018 SWIGS meeting slides, please change as needed

## Slide 2: Three elements of GIC
dB/dt from space weather: electrojets, sudden impulses, ring current, pulsations?
Induced geoelectric fields, deep into conducting Earth
Conducting networks experience induced voltages that drive GIC, following Kirchoff’s Law
Egeo
Risk scenarios (“benchmarks” in US) need parameters that reflect extreme conditions in the natural space weather environment: key science input to policy
Which element is best to provide this?

## Slide 3: dB/dt: the old way?
As used in 2012 UK reasonable worst case (5000 nT/min)
Nat Risk Assessment, RAEng report
Nat Grid correlation reported by Erinmez (2002)
State-of-art in 2012
Widely used since 1989 storm
Advance wrt Kp
Wide data availability
Values from Thomson et al (2011), & Kappenman (2006)

## Slide 4: Moving to E-fields?
Egeo
International state-of-art moving to Egeo
Prime driver of GIC
Better reflects vector nature of dB/dt and Egeo
Coastal effects
MT data more widely available
2018 UK reasonable worst case noted that Egeo is also relevant
Alongside dB/dt
>20 V/km (Beggan et al, 2013)

## Slide 5: Some questions: 1
Does use of geoelectric fields give more insight into regional variations of GIC risk?
  Do averages obscure critical detail?
  Coastal effects, especially E-fields “parallel” to coast
Does the UK need to keep up with the international state-of-the-art?
Can we improve the historical evidence base for large geoelectric fields in the UK?
  Telecomms records from storms such as May 1921 and Nov 1960?

## Slide 6: Some questions: 2
How does this fit with current UK capabilities as being developed via SWIGS?
  Promote
How do we communicate the changing state-of-the-art to a wider UK audience?
How does grid evolution affect GIC risk?
  See next slide

## Slide 7: Grid evolution
More HVDC interconnects (see map, next slide):
  more technical control?
  more risk from distant impacts?
Low carbon generation
  less intrinsic inertia (“spinning mass”) in system
  more sensitive to short-term (seconds) anomalies (see 9 August slide)
  Needs alternative technologies (e.g. battery backup, as 9 August)

## Slide 8: UK interconnects today
International:
France
Netherlands
R. Ireland
Belgium
Norway
More in planning
Internal
Scotld-Wales
Moray Firth

## Slide 9: 9 August 2019
90 secs
From Ngrid ESO interim report